## Slide 1
THOROGOOD SHOES
(A DIVISION OF THE WEINBRENNER SHOE COMPANY, USA)
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 2
PROGRAM
THE PURPOSE OF ADVANCED INSPECTION AND CLEANING IS TO HAVE TRAINED PERSONNEL PERFORM THOROUGH CLEANING ON YOUR FOOTWEAR AND EVALUATE WHETHER IT IS FIT FOR DUTY IN ITS CURRENT CONDITION
ADVANCED INSPECTION AND CLEANING MUST BE PERFORMED BY TRAINED FIRE DEPARTMENT PERSONNEL
THE GOAL OF THIS PROGRAM IS TO PROVIDE THE DEPARTMENT WITH TRAINING FOR THE INPECTION, CARE AND MAINTAINENCE OF THOROGOOD FIRE FOOTWEAR
(cont’d)
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 3
NFPA 1851 REQUIRES YOUR DEPARTMENT TO PERFORM AN ADVANCED INSPECTION AT A MINIMUM OF ONCE EVERY 12 MONTHS, OR WHENEVER A ROUTINE INSPECTION INDICATES A PROBLEM EXISTS
AN ADVANCED CLEANING IS REQUIRED EVERY 12 MONTHS OR AT THE TIME OF AN ADVANCED INSPECTION
-------
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 4
HOW TO PERFORM AN ADVANCED INSPECTION ON STRUCTURAL FIREFIGHTING FOOTWEAR THE INSPECTOR MUST DETERMINE IF:
THE FOOTWEAR IS FIT FOR DUTY
THE ITEM IS IN NEED OF REPAIR
THE ITEM NEEDS TO BE RETIRED
ALL FINDINGS FROM AN ADVANCED INSPECTION MUST BE DOCUMENTED ON AN INSPECTION FORM AND KEPT ON FILE WITH THE DEPARTMENT
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 5
TO PERFORM AN ADVANCED INSPECTION:
FOOTWEAR MUST BE CLEAN WHEN INSPECTING
PERFORM THE INSPECTION IN A CLEAN, WELL-LIGHTED AREA WITH A UTILITY SINK
LOOK FOR CUTS, TEARS OR PUNCTURES
LOOK FOR THERMAL DAMAGE
(cont’d)
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 6
TO PERFORM AN ADVANCED INSPECTION:
LOOK FOR EXPOSED OR DEFORMED STEEL TOES, MIDSOLE OR SHANK
LOOK FOR SEAM INTEGRITY, MISSING OR BROKEN STITCHES AND DELAMINATION
LOOK FOR CLOSURE SYSTEM DAMAGE AND FUNCTIONALITY PROBLEMS
(cont’d)
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 7
TO PERFORM AN ADVANCED INSPECTION:
LOOK FOR DAMAGE TO THE LINER, SUCH AS TEARS, THIN SPOTS OR SEPERATION FROM THE OUTER LAYER
LOOK FOR HEEL COUNTER FAILURE AND LOSS OF WATER RESISTANCE
------
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 8
TO PERFORM AN ADVANCED INSPECTION:
TO INSPECT FOR LEAKS:
TEAR OFF THREE 12” PIECES OF BROWN PAPER TOWELS
CRUMPLE EACH PIECE INTO A BALL
PLACE ONE BALL EACH INTO THE TOE, INSOLE AND HEEL OF EACH BOOT
PLACE BOOTS INTO 5” OF WATER AND HOLD DOWN FOR 10 SECONDS
REMOVE BOOTS FROM WATER AND REMOVE PAPER TOWELS WITH DRY HANDS
CHECK PAPER FOR WETNESS, THIS MEANS LEAKAGE
(cont’d)
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 9
TO PERFORM AN ADVANCED INSPECTION:
TO INSPECT FOR LEAKS:
IF YOU DETECT LEAKAGE, REMOVE BOOTS FROM SERVICE IMMEDIATELY AND CONTACT SUPERVISORY PERSONNEL
DOCUMENT ALL DAMAGE ON INSPECTION FORM
DO NOT RETURN TO SERVICE UNTIL IT HAS BEEN REPAIRED
ALL REPAIRS MUST BE MADE BY THE MANUFACTURER OR A VERIFIED ISP
-------
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 10
TO PERFORM AN ADVANCED CLEANING:
WEAR PROTECTIVE GLOVES AND EYE/FACE SPLASH PROTECTION
PRE-TREAT SEVERELY SOILED BOOTS WITH A CITRUS-BASED DEGREASER
DO NOT USE PETROLEUM-BASED DEGREASER
APPLY DEGREASER ACCORDING TO DIRECTIONS
ALLOW DEGREASER TO SOAK INTO THE STAIN
(cont’d)
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 11
TO PERFORM AN ADVANCED CLEANING:
GENTLY SCRUB WITH A SOFT BRISTLE BRUSH
FOR GLOBS OF TAR, USE PLASTIC OR WOOD SCRAPPER
WARM WATER SHOULD NOT EXCEED 105 DEGREES F
-------
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 12
TO PERFORM A GENERAL CLEANING:
FILL SINK WITH 6” OF WATER
WATER SHOULD NOT EXCEED 105 DEGREES F
ADD 2 SQUIRTS OF LIQUID DISH SOAP OR SPECIALTY PPE CLEANER
NEVER USE CHLORINE OR CHLORINE BASED PRODUCT
PLACE BOOTS IN SINK
BRUSH BOOTS WITH SOFT BRISTLE BRUSH UNTIL DIRT IS REMOVED
(cont’d)
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 13
TO PERFORM A GENERAL CLEANING:
RINSE AWAY ALL SOAP AND DIRT FROM BOOTS
REMOVE EXCESS MOISTURE WITH SOFT CLOTH OR TOWEL
LET BOOTS AIR-DRY ON RACK IN A DRY, WELL-VENTILATED ROOM AWAY FROM SUNLIGHT
DO NOT PLACE BOOT NEAR A HEAT SOURCE WHEN DRYING
NEVER USE BLOW DRYER, HEAT GUN OR SPACE HEATER TO ACCELERATE DRYING OF BOOTS
CONDITION BOOTS WITH BOOT PASTE OR BOOT CONDITIONER
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 14
RETIREMENT:
AFTER INSPECTION/CLEANING/REPAIR, IF THE BOOTS ARE DETERMINED BY THE APPROVED TRAINED PERSONNEL THAT THE BOOTS ARE NOT FUNCTIONAL TO PERFORM THE MISSION, THE BOOTS SHOULD BE RETIRED ACCORDING TO NFPA 1851
ALL STRUCTURAL BOOTS ARE TO BE RETIRED 10 YEARS FROM THE DATE OF MANUFACTURE AS PER NFPA 1851
THOROGOOD SHOES
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM

## Slide 15
I, _________________________ , certify that all appropriate parties in the department
PRINT NAME
have read and understand the inspection, care and maintenance procedures described in this NFPA 1851 inspection, care and maintenance course.
Upon receiving this completed form, The Weinbrenner Shoe Company, USA will sign and return a copy for the department’s records.
___________________ _____________________
Department Signature Date The Weinbrenner Shoe Company, USA Signature Date
UPON COMPLETETION OF THIS PROGRAM, PLEASE PRINT, FILL OUT, SIGN AND RETURN THIS PAGE TO:
The Weinbrenner Shoe Company, USA
Attn: Dawn Osness, 108 S Polk St., Merrill, WI 54452
NFPA 1851 ADVANCED INSPECTION, CARE AND MAINTENANCE CERTIFICATION PROGRAM